## Slide 1
Website: https://operalab.pusan.ac.kr/
GitHub: https://github.com/SimFL-Lab
Email: soondo.hong@pusan.ac.kr
Google Scholar: https://bit.ly/SoondoHongGoogleScholar
Phone: +82-51-510-2331
A dynamic storage location assignment model for a progressive bypass zone picking system with an S/R crane
Jeonghwan Kim and Soondo Hong
Objective
This paper optimizes the storage locations with consideration of workload imbalance and reduction of recirculation in a progressive bypass zone picking system. This paper also suggests a dynamic storage location assignment when the system has a limited material handling capacity.
Contribution
This paper develops an SLA model that considers both workload balance and recirculation reduction, and an SLR model that switches pairs of products in warehouses with limited material handling capacity.
Model Formulation
Proposing a mixed-integer programming model (MIP), the Storage location assignment (SLA) model that assigns the entire product list.
Proposing a MIP-based storage location reassignment (SLR) model that relocates products for the allowed number of relocation operations.
Experimental Design
Key Findings
A framework for a storage assignment was provided to improve order picking throughput by using the number of picks per zone, and the number of order visits per zone to consider workload balance between zones and each zone’s waiting time.
SLA is preferable for long-term planning over monthly and seasonal changes, and SLR is preferable for daily changes because it modulate daily demand fluctuation with relatively little effort.
Designing the experiment by considering these following configurations:
Peroformance measurements:
Order size
CONWIP level
Num of relocation operations
Num of zones
Num of products
Num of orders
Objective value
Computation time
Average cycle time
Makespan

## Slide 2
Website: https://operalab.pusan.ac.kr/
GitHub: https://github.com/SimFL-Lab
Email: soondo.hong@pusan.ac.kr
Google Scholar: https://bit.ly/SoondoHongGoogleScholar
Phone: +82-51-510-2331
Batch Assorting for Worker-following Assortment Carts in Parallel-aisle Order-assorting Systems
Taehoon Lee, Jeongman Lee, and Soondo Hong
Objective
This study introduces an order-assorting system (OAS) in a distribution center. The system supports assortments with worker-following carts loading SKUs from a depot and unload them at the convenience stores’ designated cells in the OAS.
Contribution
Formulating a mixed-integer programming (MIP) model for binning and batching operations which minimizes the total travel distance of cart in small-sized problems.
Proposing the route packing-based heuristic to solve a practical situation in large-sized problems with the binning and batching operations in the OAS.
Model Formulation
Proposing two mixed-integer programming model (MIP), the batching-only model (BOM) and the binning and batching model (BBM) with three types of constraints.
Proposing the route packing-based binning then batching (RPBB) heuristic to solve a large-sized BBM problem consisting of a binning procedure based on route packing (BPM-RP) and a batching procedure using a simple integer programming formulation.
Experimental Design
Key Findings
This paper reveals that BBM minimizes the total travel distance of carts for the OASs that use worker-following cart systems.
By proposing BBM and RPBB that shorten the total travel distance by optimizing the balance between binning and batching, this result indicates that RPBB obtains near-optimal solutions by the tight lower bound and can solve large-sized problem.
Deploying the small-sized problems to compare the heuristic algorithm with BBM and the large-sized problems to compare the heuristic algorithm with the lower bound.
Testing the heuristic algorithm against the performance for various problem sizes.
Designing the experiments by considering the number of SKUs, volume of SKUs, routing policy, number of aisles, length of aisles, distance between two adjacent aisles, and capacity of a worker-following cart (CAPA).